## Slide 1
C A R I A D
AEB
Autonomous Emergency Braking | 自动紧急制动系统
WHAT IS AEB?
AEB (Autonomous Emergency Braking) is an advanced driver assistance system that automatically applies the brakes when a collision is imminent and the driver fails to respond in time.
HOW IT WORKS
1 SENSE
Radar, camera & LiDAR sensors continuously monitor the road ahead for vehicles, pedestrians & obstacles.
2 DECIDE
ECU evaluates collision risk based on relative speed, distance & trajectory — triggering alerts then braking.
3 ACT
If the driver does not react, the system autonomously applies full braking force to avoid or mitigate collision.
AEB IN ACTION
EGO
TARGET
distance < threshold
!
BRAKE
RADAR
CAMERA
Collision risk detected → Autonomous braking engaged
KEY BENEFITS
● Reduces rear-end collisions by up to 50% (Euro NCAP)
● Operates at city & highway speeds (5–250 km/h)
● Detects vehicles, pedestrians, cyclists & static obstacles
● Mandatory for all new vehicles in EU since 2024
-50%
Collision Reduction
< 0.5s
System Response
5-250 km/h
Speed Range
2024+
EU Mandatory
INTERNAL / CONFIDENTIAL | CSD class: 2.5

## Slide 2
C A R I A D
C-NCAP 2027 AEB 测试场景总览
AEB / FCW / AES | 车对弱势道路使用者 + 车对车 | 基础 + 拓展场景
附录P — VRU / 弱势道路使用者保护
车对行人 Car-to-Pedestrian (CPTA)
纵行/横穿/转弯/低速/高速/雨天/遮挡/干扰 — 12场景
车对二轮车 Car-to-2Wheeler
电动自行车纵行/斜向/横穿/切入 + 自行车近端 + 踏板摩托远端/转弯 — 14场景
车对三轮车 Car-to-TriWheeler
追尾切入/横穿/转弯对撞 — 3场景
功能覆盖
AEB + FCW + AES (自动紧急转向)
附录Q — C2C / 车对车 ADAS 测试
基础场景 (6项 · 必测)
CCRc 切入追尾 / CCRh 高速追尾 / CCRb 制动追尾 / C2C SCPf 远端横穿 / CCFT 转弯对撞 / CCRbc 弯道制动
拓展场景 (10项 · 抽测验证)
CCRsr 雨天追尾 / CCRsf 雾天追尾 / CCFhos 直行对撞 / C2C SCPn 近端横穿 / SCPmo 动态遮挡横穿 / CCFTf 跟车转弯对撞 / LCPf/LCPn 左转横穿 / RCPf 右转横穿 / SCPso 静态遮挡横穿
测试速度范围
基础: 40–120 km/h | 拓展: 30–120 km/h
功能覆盖
AEB + FCW + AES + LKA + ELK + DMS + BSD + DOW + RCTB + ISLS + AMAP
6+10
车对车测试场景 (必测+抽测)
30+
VRU 测试场景 (行/二轮/三轮)
0–120 km/h
测试速度范围
2027
C-NCAP 版本
INTERNAL / CONFIDENTIAL | CSD class: 2.5 | Source: C-NCAP 2027 Management Rules